0 12 1001 01310 0105

Elementally geometrical L-shaped handle with a cylindrical neck joined to a grip of square cross-section

Design: Peter Bastian

Grip cross-section 21x21mm, handle length 135mm, handle neck dia. 24mm

EN 179 variant 1002 as U-shaped handle

The products quoted for are to have been manufactured under a process certified to ISO 140125 as well as to EMAS/EN ISO 14001 and governed by a Quality Management System as laid down in EN ISO 9001. The relevant certificates are to be furnished.

Lever handle furniture for doors with no special requirements. Design variant: circular rose

Item description: L-shaped handle design in which a circular shank passes over into a sturdy rectangular grip, length of grip section approx. 135mm

The design of the lever handle and knob is also prescribed for window handles and frame-door fittings.

Concealed fixing

Classification key under  EN 1906:

- for with no special requirements:  4 | 7 | - | 0 | 1 | 4 | 0 | A

- positive-locking connection of the two female handles by means of cup point screws and adapter-system roses for optimized absorption by the door leaf of forces exerted

- dimensional specifications as under DIN 18255 with handle shank bearing dia. 18mm and shank length t > 7mm

- adaptor-system furniture with inseparable sliding bearings

- handle roses with stainless steel bases

Handle and cylinder roses with 8.5mm reinforcement lugs and sliding bearings to absorb any tensile, compressive and torsional forces arising

Circular roses dia. approx. 55mm, height approx. 7mm, edge radius approx. 1mm, screw centres 38mm, concealed through

fixing with M5 screws

8mm spindle

PC = for European profile cylinder

Silver Anodised Aluminium